Pump Optimization Example

Inputs

O&M Tab

- Choose kWh from Electricity pull down menu

- Current delivered price per physical unit - $.08

- Current annual consumption in physical units – 246,667

- Proposed annual consumption in physical units – 209,667

- Maintenance

  - Current Application - $10,000

  - Proposed Application - $3,340

Capital Tab

- Economic life of this investment, in years – 25

- Cost of Capital or Minimum Rate of Return – 7%

- Annual excalation factor for energy prices – 2.5%

- Simple Payback Target (years) – 1 year

- Return on Investment (ROI) – 20%

- Construction and/or equipment costs - $16,000

Outputs

|  | INVESTMENT CRITERIA |  | CALCULATED | TARGET |
| --- | --- | --- | --- | --- |
|  | SIMPLE PAYBACK: |  | = 1.7 years | 1.0 years |
|  | RETURN ON INVESTMENT: |  | 82.15% | 20.0% |
|  | LIFE-CYCLE COST (25 YEARS) |  | $720,953 |  |
|  | NET PRESENT VALUE: |  | $124,754 |  |
|  | INTERNAL RATE OF RETURN: |  | 62.6% |  |
|  | ANNUALIZED COST TO SAVE 1 MMBtu: |  | $10.75 |  |
|  | COST TO BUY 1 MMBtu: |  | $23.45 |  |